## Slide 1: Advanced Computational Methods in Geotechnical Engineering
Finite Difference Method (FDM)

## Slide 2
Consolidation Settlement and
Average Degree of Consolidation - FD Solution
Conventional consolidation settlement analysis using empirical equations has the following limitations:
  The coefficient of consolidation Cv is assumed to be constant, however, it is well known that Cv changes with time in the consolidation process.
  Variation in application of load such as stage loading (load increasing by a certain rate), and abrupt change of load (the case of surcharge preloading) are not considered.

## Slide 3
Consolidation Settlement…
Numerical solution using the finite difference method can be used to overcome the problem.
The numerical solution does not require the empirical correlation for Tv because it can be done by using the original formula and load application and other variations can be modeled almost correctly.

## Slide 4
Consolidation Settlement…
(A)
When the pore pressures is completely dissipated.
Average degree of consolidation

## Slide 5
Consolidation Settlement…
In Eqn. (A), the integral of the excess pore pressure cannot be evaluated exactly because the excess pore pressure is only at the grid points.
However, the integral can be evaluated approximately using some numerical techniques. The simplest approach is to use the Trapezoidal Method.

## Slide 6
Variable Loading
In reality, a loading is never placed instantaneously and the problem can be easily handled through finite difference formulation.
Variable loading usually occurs when there is a structure being built on top of the soil layer. As the construction of the structure proceeds, the load induced onto the ground gradually increases with time.

## Slide 7
…Variable Loading
Considering that the construction is a time consuming process, we cannot assume a formulation of instantaneous load to be used in the calculation of settlement.

## Slide 8
Abrupt Change of Load
When the existing soil layers are too weak, it has to be loaded in stages. Loading in stages will increase the shear strength and bearing capacity of the soil as it consolidates.

## Slide 9
Variable Coefficient of Consolidation (Cv)
The coefficient of consolidation is usually considered as constant in consolidation analysis although it is a variable quantity.
It is known empirically that CV changes during consolidation as the void ratio of the soil changes causing a decrease in permeability and compressibility of the soil.

## Slide 10
Example
Drainage
Boundary
Analyze the pore water pressure, settlement and average degree of consolidation of the soil layer after 2 years of consolidation using FDM.

## Slide 11
Example
Case 1: constant load scenario: a uniform load of 90 kPa is applied onto the soil layer at once.
Settlement (mm) | 0.0 | ※ |  |  |  |  |  |  |  |  | 
t(yrs) | 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0
q(kPa) | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
z=0 m | 0 | ※ |  |  |  |  |  |  |  |  | 
z=1 m | 90 | ※ |  |  |  |  |  |  |  |  | 
z=2 m | 90 | ※ |  |  |  |  |  |  |  |  | 
z=3 m | 90 | ※ |  |  |  |  |  |  |  |  | 
z=4 m | 90 | ※ |  |  |  |  |  |  |  |  | 
Uav(%) | 0.0 | ※ |  |  |  |  |  |  |  |  | 

## Slide 12
Example
Case 1: constant load scenario: a uniform load of 90 kPa is applied onto the soil layer at once.
Settlement (mm) | 0.0 |  |  |  |  |  |  |  |  |  | 
t(yrs) | 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0
q(kPa) | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
z=0 m | 0 | 0 |  |  |  |  |  |  |  |  | 
z=1 m | 90 | 54 |  |  |  |  |  |  |  |  | 
z=2 m | 90 | 90 |  |  |  |  |  |  |  |  | 
z=3 m | 90 | 90 |  |  |  |  |  |  |  |  | 
z=4 m | 90 | 90 |  |  |  |  |  |  |  |  | 
Uav(%) | 0.0 |  |  |  |  |  |  |  |  |  | 

## Slide 13
Example
Case 2: variable load scenario: a fill having a unit weight 15 kN/m3 is placed at a rate of 0.5 m/month during the first year and the filling stops after one year. The final load would be 90 kPa.
Settlement (mm) | 0 | ※ |  |  |  |  |  |  |  |  | 
t(yrs) | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
q(kPa) | 0 | 9 | 18 | 27 | 36 | 45 | 54 | 63 | 72 | 81 | 90
z=0 m | 0 | ※ | ※ |  |  |  |  |  |  |  | 
z=1 m | 0 | ※ | ※ |  |  |  |  |  |  |  | 
z=2 m | 0 | ※ |  |  |  |  |  |  |  |  | 
z=3 m | 0 | ※ |  |  |  |  |  |  |  |  | 
z=4 m | 0 | ※ |  |  |  |  |  |  |  |  | 

## Slide 14
Example
Case 2: variable load scenario (continued):
Settlement (mm) |  |  |  |  |  |  |  |  |  | 
t(yrs) | 1.1 | 1.2 | 1.3 | 1.4 | 1.5 | 1.6 | 1.7 | 1.8 | 1.9 | 2.0
q(kPa) | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
z=0 m |  |  |  |  |  |  |  |  |  | 
z=1 m |  |  |  |  |  |  |  |  |  | 
z=2 m |  |  |  |  |  |  |  |  |  | 
z=3 m |  |  |  |  |  |  |  |  |  | 
z=4 m |  |  |  |  |  |  |  |  |  | 
Uav(%) |  |  |  |  |  |  |  |  |  | 

## Slide 15
Example
Case 2: variable load scenario: a fill having a unit weight 15 kN/m3 is placed at a rate of 0.5 m/month during the first year and the filling stops after one year. The final load would be 90 kPa.
Settlement (mm) | 0 | 3.735 |  |  |  |  |  |  |  |  | 
t(yrs) | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1.0
q(kPa) | 0 | 9 | 18 | 27 | 36 | 45 | 54 | 63 | 72 | 81 | 90
z=0 m | 0 | 0 | 0 |  |  |  |  |  |  |  | 
z=1 m | 0 | 9 | 16.2 |  |  |  |  |  |  |  | 
z=2 m | 0 | 9 |  |  |  |  |  |  |  |  | 
z=3 m | 0 | 9 |  |  |  |  |  |  |  |  | 
z=4 m | 0 | 9 |  |  |  |  |  |  |  |  | 

## Slide 16
Example
Case 3: abrupt change of load scenario: In the abrupt change of load scenario, the soil layer will be loaded with fill of 60 kPa and after one year, an additional fill of 30 kPa will be laid on the existing fill.
Settlemnt (mm) |  |  |  |  |  |  |  |  |  |  | 
t(yrs) | 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0
q(kPa) | 60 | 60 | 60 | 60 | 60 | 60 | 90 | 90 | 90 | 90 | 90
z=0 m | 0.0 |  |  |  |  |  |  |  |  |  | 
z=1 m | 60 |  |  |  |  |  |  |  |  |  | 
z=2 m | 60 |  |  |  |  |  |  |  |  |  | 
z=3 m | 60 |  |  |  |  |  |  |  |  |  | 
z=4 m | 60 |  |  |  |  |  |  |  |  |  | 
Uav(%) | 0.0 |  |  |  |  |  |  |  |  |  | 

## Slide 17
Example
Case 4: constant Load with Variable Cv: the Cv is assumed to decrease with a rate of 0.1 m2/year.
Settlemnt (mm) |  |  |  |  |  |  |  |  |  |  | 
CV | 2.0 | 1.98 |  |  |  | 1.9 |  |  |  |  | 1.8
t(yrs) | 0 | 0.2 | 0.4 | 0.6 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0
q(kPa) | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90 | 90
z=0 m | 0.0 |  |  |  |  |  |  |  |  |  | 
z=1 m | 90 |  |  |  |  |  |  |  |  |  | 
z=2 m | 90 |  |  |  |  |  |  |  |  |  | 
z=3 m | 90 |  |  |  |  |  |  |  |  |  | 
z=4 m | 90 |  |  |  |  |  |  |  |  |  | 
Uav(%) | 90 |  |  |  |  |  |  |  |  |  |