## Slide 1
  Course Title: Advanced Finite Element Method and Finite Difference Method in Geotechnical Engineering
  Course Code: CENG 8203
  Credit Hours: 3
  Program: Regular
  Semester: I
  Course Instructor: Dr. Tensay G.
  University: Addis Ababa Science and Technology

## Slide 2: General of FE programs
11/30/2012

## Slide 3: General Overview

## Slide 4: General Overview

## Slide 5: General Overview

## Slide 17: II - WTG FOUNDATION DESIGN AND CONSTRUCTION

## Slide 21: 1.* Introduction to MATLAB
MATLAB is an interactive, matrix-based system for scientific and engineering numeric computation and visualization.
You can solve complex numerical problems in a fraction of the time required with a programming language such as Fortran or C.
The name MATLAB is derived from MATrix LABoratory.
Accessing MATLAB.
On most systems, after logging in one can enter MATLAB with the system command matlab and exit MATLAB with the MATLAB command quit or exit.

## Slide 22: 1.* Introduction to MATLAB ... Cont‘d
Entering matrices
MATLAB works with essentially only one kind of object;
  a rectangular numerical matrix with possibly complex entries
  all variables represent matrices.
In some situations, 1-by-1 matrices are interpreted as scalars and matrices with only one row or one column are interpreted as vectors.

## Slide 23: 1.* Introduction to MATLAB ... Cont‘d
Matrices can be introduced into MATLAB in several different ways:
  Entered by an explicit list of elements,
  Generated by built-in statements and functions,
  Loaded from external data files or applications
Elements separators may be commas as well as a blank space.
Caution is required when listing a number in exponential form. (e.g. 2.34e-9)

## Slide 24: 1.* Introduction to MATLAB ... Cont‘d
MATLAB allows complex numbers in all its operations and functions.
Complex numbers can be entered in a convenient way as:
B = [1+5i 2+6i;3+7i 4+8i]
When listing complex numbers (e.g. 2+6i) in a matrix, blank spaces must be avoided.
Either i or j may be used as the imaginary unit. If, however, you use i and j as variables and overwrite their values, you may generate a new imaginary unit.
Matrices can also be generated with a for-loop

## Slide 25: 1.* Introduction to MATLAB ... Cont‘d
Matrices can also be generated with a for-loop
Individual matrix and vector entries can be referenced with indices inside parentheses in the usual manner.
For example, A(2, 3) denotes the entry in the second row, third column of matrix A and x(3) denotes the third coordinate of vector x. Try it.
A matrix or a vector will only accept positive integers as indices.

## Slide 26: 1.* Introduction to MATLAB ... Cont‘d
Matrix /Array operations
The following matrix operations are available in MATLAB:
    + addition
    - subtraction
    * multiplication
    ^ power
    ‘ conjugate transpose
    \ left division
    / right division
These matrix operations apply, of course, to scalars (1-by-1 matrices) as well.
If the sizes of the matrices are incompatible for the matrix operation, an error message will result

## Slide 27: 1.* Introduction to MATLAB ... Cont‘d
The " matrix division" operations deserve special comment.
  If A is an invertible square matrix and b is a compatible column, resp. row, vector, then x = A/b is the solution of A*x = b and, resp., x = b\A is the solution of x * A = b.
Array operations.
The matrix operations of addition and subtraction already operate entry-wise but …
It is important to observe that the other operations, *, ^, /, and \, can be made to operate entry-wise by preceding them by a period.
For example, either [1,2,3,4].*[1,2,3,4] or [1,2,3,4].^ 2 will...

## Slide 28: 1.* Introduction to MATLAB ... Cont‘d
Statements, expressions, and variables
MATLAB is an expression language; the expressions you type are interpreted and evaluated.
MATLAB statements are usually of the form:
variable = expression, or simply
expression
Expressions are usually composed from operators, functions, and variable names.
Evaluation of the expression produces a matrix, which is then displayed on the screen and assigned to the variable for future use.

## Slide 29: 1.* Introduction to MATLAB ... Cont‘d
If the variable name and = sign are omitted, …
Several statements can be placed on a single line if separated by commas or semicolons.
If the last character of a statement is a semicolon, the printing is suppressed, but the assignment is carried out.
This is essential in suppressing unwanted printing of intermediate results.

## Slide 30: 1.* Introduction to MATLAB ... Cont‘d
MATLAB is case-sensitive in the names of commands, functions, and variables.
List of variables currently in the workspace can be… who (or whos).
A variable can be cleared from the workspace with the command clear variablename. The command clear alone will clear all nonpermanent variables.
The permanent variable eps (epsilon) gives the machine unit round-off about 10E-16 on most machines. (for convergence)
A runaway display or computation can be stopped...

## Slide 31: 1.* Introduction to MATLAB ... Cont‘d
Matrix building functions
Some important convenient matrix building functions are:
  eye - identity matrix
  zeros - matrix of zeros
  eig – eigenvlaues of a matrix
  [C,D] eig(A)-
  ones - matrix of ones
  diag - create or extract diagonals
  triu - upper triangular part of a matrix
  tril - lower triangular part of a matrix

## Slide 32: 1.* Introduction to MATLAB ... Cont‘d
For example, zeros(m,n) produces an m-by-n matrix of zeros
zeros(n) produces an n-by-n one.
If A is a matrix, then zeros(size(A)) produces a matrix of zeros having the same size as A.
If x is a vector, diag(x) is the diagonal matrix with x down the diagonal
If A is a square matrix, then diag(A) is a vector consisting of the diagonal of A. What is diag(diag(A))? Try it.

## Slide 33: 1.* Introduction to MATLAB ... Cont‘d
Matrices can be built from blocks.
For example, if A is a 3-by-3 matrix, then B = [A, zeros(3,2); zeros(2,3), eye(2)] will build .... Try it.
For, while, if - and relations.
In their basic forms, these MATLAB flow control statements operate like those in most computer languages.
For
For example, for a given n, the statement
x = [ ]; for i = 1:n, x=[x,i^2], end
Or
x = [ ];
for i = 1:n
x = [x,i^2]
end

## Slide 34: 1.* Introduction to MATLAB ... Cont‘d
The statements
    for i = 1:m
    for j = 1:n
    H(i, j) = 1/(i+j-1);
    end
    end
    H
The semicolon on the inner statement … unwanted intermediate results while the last H displays the final result.
    s = 0;
    for d = A
    s = s + sum(d);
    end

## Slide 35: 1.* Introduction to MATLAB ... Cont‘d
While
The general form of a while loop is
  While relation
  statements
  End
The statements will be repeatedly executed as long as the relation remains true. 2n >= a … :
  n = 0;
  while 2^n < a
  n = n + 1;
  end
  n

## Slide 36: 1.* Introduction to MATLAB ... Cont‘d
If
The general form of a simple if statement is
  if relation
  statements
  end
Multiple branching is also possible, as is illustrated by
  if n < 0
  number = ‘Negtive’;
  elseif rem(n,2) == 0
  number = ‘Even positive’;
  else
  number = ‘Odd Positive’;
  end

## Slide 37: 1.* Introduction to MATLAB ... Cont‘d
Relations.
The relational operators in MATLAB are
  < less than
  > greater than
  <= less than or equal
  >= greater than or equal
  == equal
  ~= not equal.
Note that ‘’=" is used in an assignment statement while ‘’==" is used in a relation.
Relations may be connected or quantified by the logical operators
  & and
  | or
  ~ not.

## Slide 38: 1.* Introduction to MATLAB ... Cont‘d
Scalar functions.
Certain MATLAB functions operate essentially on scalars, but operate element-wise when applied to a matrix.
The most common such functions are:
  sin asin exp abs round
  cos acos log (natural log) sqrt floor
  tan atan rem (remainder) sign ceil
Vector functions.
A few of these functions are:
  max sum median any
  Min prod mean all
  sort std

## Slide 39: 1.* Introduction to MATLAB ... Cont‘d
Matrix functions.
Much of MATLAB's power comes from its matrix functions. The most useful ones are:
  eig eigenvalues and eigenvectors
  chol cholesky factorization
  inv inverse
  lu LU factorization
  expm matrix exponential
  sqrtm matrix square root
  poly characteristic polynomial
  det determinant
  size size
  rank rank

## Slide 40: 1.* Introduction to MATLAB ... Cont‘d
MATLAB functions may have single or multiple output arguments. For example,
y = eig(A), or simply eig(A)
produces a column vector containing the eigenvalues of A while
[U,D] = eig(A)
produces a matrix U whose columns are the eigenvectors of A and a diagonal matrix D with the eigenvalues of A on its diagonal. Try it.
Submatrices and colon notation.
Vectors and submatrices are often used in MATLAB to achieve fairly complex data manipulation effects.

## Slide 41: 1.* Introduction to MATLAB ... Cont‘d
Colon notation:
used both to generate vectors and reference submatrices.
Creative use of these features to vectorize operations permits one to minimize the use of loops (which slows MATLAB) and to make code simple and readable.
The expression 1:5 (met earlier in for statements) is actually the row vector [1 2 3 4 5].

## Slide 42: 1.* Introduction to MATLAB ... Cont‘d
The numbers need not be integers nor the increment one.
For example, 0.2:0.2:1.2 gives [0.2, 0.4, 0.6, 0.8, 1.0, 1.2], & 5:-1:1 gives [5 4 3 2 1].
The following statements will, for example, generate a table of sines. Try it.
      x = [0.0:0.1:2.0]’;
      y = sin(x);
      [x y]

## Slide 43: 1.* Introduction to MATLAB ... Cont‘d
The colon notation can be used to access submatrices of a matrix. For example, A(1:4,3) is the column vector consisting of the first four entries of the third column of A.
A colon by itself denotes an entire row or column:
A(:,3) is the third column of A, and A(1:4,:) is the first four rows.
Arbitrary integral vectors can be used as subscripts:
A(:,[2 4]) contains as columns, columns 2 and 4 of A.
Such subscripting can be used on both sides of an assignment statement:
A(:,[2 4 5]) = B(:,1:3) replaces columns 2,4,5 of A with the first three columns of B.

## Slide 44: 1.* Introduction to MATLAB ... Cont‘d
M-files.
MATLAB can execute a sequence of statements stored in diskfiles.
Such files are called M-files" because they must have the file type of .m as the last part of their filename.
Much of your work with MATLAB will be in creating and refining M-files. M-files are usually created using your local editor.
There are two types of M-files: script files and function files.

## Slide 45: 1.* Introduction to MATLAB ... Cont‘d
Graphics.
MATLAB can produce planar plots of curves, 3-D plots of curves & 3-D mesh, surface plots.
The primary commands for these facilities are plot , plot3, mesh, and surf resp.
Planar plots:#,
The plot command creates linear x-y plots; if x and y are vectors of the same length, the command plot(x,y) opens a graphics window and draws an x-y plot of the elements of x versus the elements of y.
One can draw the graph of the sine function over the interval -4 to 4 with the following commands:
x = -4:.01:4; y = sin(x); plot(x,y) Try it.

## Slide 46: 1.* Introduction to MATLAB ... Cont‘d
Linetypes: solid (-), dashed (--). dotted (:), dashdot (-.)
Marktypes: point (.), plus (+), star (*), circle (o), x-mark (x)
Colors can be specified for the line- and mark-types.
Colors: yellow (y), magenta (m), cyan (c), red (r), green (g), blue (b), white (w), black (k)
For example:
x = -1.5:.01:1.5; y = exp(-x.^2); plot(x,y, 'r--')

## Slide 47: 1.2 Computational Mechanics

## Slide 48: 1.2 Computational Mechanics…

## Slide 49: 1.2 Computational Mechanics…

## Slide 50: 1.2 Computational Mechanics…

## Slide 51: 2.1.1 FEM Variants
2.1 Introduction to Finite Element Method
  2 FINITE ELEMENT METHOD

## Slide 54: 2.1.2 FEM Analysis Process

## Slide 55: 2.1.3 Interpretations of FEM

## Slide 60
Types of Finite Elements
  2.2 1D Finite element

## Slide 61
2.2.1 Spring Element
  2.2 1D Finite element

## Slide 62
  2.2 1D Finite element

## Slide 63
  2.2 1D Finite element

## Slide 64
  2.2 1D Finite element

## Slide 65
  2.2 1D Finite element

## Slide 66
  2.2 1D Finite element

## Slide 67
  2.2 1D Finite element

## Slide 68
  2.2 1D Finite element

## Slide 69
  2.2 1D Finite element

## Slide 70
  2.2 1D Finite element

## Slide 71
  2.2 1D Finite element

## Slide 72
  2.2 1D Finite element

## Slide 73
  2.2 1D Finite element

## Slide 74
  2.2 1D Finite element

## Slide 75
  2.2 1D Finite element

## Slide 76
  2.2 1D Finite element

## Slide 77
  2.2 1D Finite element

## Slide 78
  2.2 1D Finite element

## Slide 79
Steps to be followed:
Step-1: discretizing the domain
Step-2: Writing the ESM
Step-3: Assembling the GSM
Step-4: Applying the BCs
Step-5: Solving the Eqns
Step-6: Post processing
  2.2 1D Finite element

## Slide 80
  2.2.2 Bar and Beam Element

## Slide 93
Exercise:
Check your solution obtained above if the load P is reduced by half

## Slide 94
  2.3 2D Finite Element

## Slide 95
  2.3 2D Finite Element

## Slide 96
  2.3 2D Finite Element

## Slide 97
  2.3 2D Finite Element

## Slide 98
  2.3 2D Finite Element

## Slide 99
  2.3 2D Finite Element

## Slide 100
  2.3 2D Finite Element

## Slide 101
  2.3 2D Finite Element

## Slide 102
  2.3 2D Finite Element

## Slide 103
  2.3 2D Finite Element

## Slide 104
What if, there is a hole inside?
  2.3 2D Finite Element

## Slide 105
  2.3 2D Finite Element

## Slide 106
  2.3 2D Finite Element

## Slide 107
  2.3 2D Finite Element

## Slide 108
  2.3 2D Finite Element

## Slide 109
  2.3 2D Finite Element

## Slide 110
  2.3 2D Finite Element

## Slide 111
  2.3 2D Finite Element

## Slide 112
  2.3 2D Finite Element

## Slide 113
  2.3 2D Finite Element

## Slide 114
Natural Coordinate
  2.3 2D Finite Element

## Slide 115
  2.3 2D Finite Element

## Slide 116
  2.3 2D Finite Element

## Slide 117
  2.3 2D Finite Element

## Slide 118
  2.3 2D Finite Element

## Slide 119
  2.3 2D Finite Element

## Slide 120
  2.3 2D Finite Element

## Slide 121
  2.3 2D Finite Element

## Slide 122
  2.3 2D Finite Element

## Slide 123
  2.3 2D Finite Element

## Slide 124
  2.3 2D Finite Element

## Slide 128
Step-1: Discritize the Domain
Step-2: Develop ESM
  Example:

## Slide 130
Step-3: Assembling the GSM
The problem has 4 nodes and hence 8 dof (8x8 matrix)

## Slide 132
Step-4: Apply BC (Refer to paper)
Step-5: Solve (thru partitioning)

## Slide 133
Step-6: Post-processing

## Slide 135
Principal stresses and angle

## Slide 138
Bilinear Quadrilateral Element

## Slide 145
Linear Tetrahedral (solid) Element